Instructions for upgrading Talon A830 from 59.0E.27.01 to 59.0F.11 software

Instruction version 1.0 (The “.gz” files stored on the website, need to be unzipped)

1. Remove the MMC card from the side of the phone if present.

2. Press “#” and “*” keys together and while doing so, ALSO press the power button (This puts the phone into what is called “FORCED FLASH MODE”).

3. Read version of the Bootloader program from the screen. If the version is older than 0.5.1.0, please flush first the bootloader_520_flash.shx program. Now, the phone is ready to continue with the upgrade.

4. Use PST Version 6.0 or higher to flash TALON_U_59.0F.02I_PDS_stepping_stone_flash.shx file.

5. After flashing, turn the unit on.  The phone will power-up, and then it will automatically enter flash mode.  This process is quick (approximately 1 second).  Note when powering up, the unit must be allowed to power up in normal mode and must NOT BE PUT IN “FORCED FLASH MODE”  (e.g. do NOT put the phone in flash mode by using the special flash USB cable - with option 1/2 pins shorted on USB cable - or by holding the * # keys while power is applied).  Once the unit has powered up and has entered flash mode, the PDS upgrade is complete.

6. After completing the power-up, flash in the TALON_U_59.0F.11I.flash.shx software.

7. Clean the old Kjava midlets in the phone. You can clean out the old midlets one of two ways.

Manually:

Go to Menu -> Settings -> Other Settings -> Java Tools

Type "CLEAN" (25326)

Go to Back -> Back -> Back -> Games & Apps

The message "Please Wait…" should appear for about 30 seconds

The message "No installed Kjava midlets suites" will then come up. Phone is now clean and can have midlets re-installed.

Automatically:

Flex the following file clear_dav_all_fs.hs.  It will delete the presence of Kjava midlets from your phone, but make sure you do your customer flex immediately AFTER doing this step (without turning off phone). You may have to flex clear_dav_all_fs.hs file using Radiocom program  v4.1 or higher (select 3G for MA and use Tab 2 to find flex utility to program using this option) if PST Phone Programmer does not load this flex file.

8. Load in the Customer flex in this step. The version to use is SA0707A021.hs

9. Next you can flash in the language package, umts_lang0027.flash.shx.

10. Next you can flash and flex in the .shx and .hs files: AU_HB_BS_0.1.3_59.0F.11.shx,  AU_HB_BS_0.1.3_59.0F.11.hs  for the Kjava midlet.

11. Perform the master reset and master clear user commands. Security code is six zero’s “000000”

12. You can check all the all latest versions are installed by looking in Settings>Phone Status >Other Information menu option. Manually check to see if Kjava midlet is present in the phone (under the Games and Apps Icon). If you have a 3G live SIM card please run the Kjava midlet ‘3 Services’ to make sure it installs/runs properly.

13. Completed.