R57_G_10.07.05R Flash Flex Procedure

This release can only be used on P3 HW with EDGE Thermistor (Build code >= 035).

WARNING: Customers BP flexes are subsidy locked, be sure to set the subsidy unlock password to 0 before flashing them.

Seem element:	SEEM_SUBSIDY_LOCK_GSM_NWSCP (id 349, offset 0)

(0x00,0x00,0x00,0x00)   // Password 00000000

Or directly use the following mini flex: reset_subsidy_password.hs

WARNING: Starting release R57_G_10.06.45I AP logging capability / telnet have been disable. See section 5 “How to activate AP logging capability/telnet” to enable it.

This release is based on

AP: EZXBASE_N_00.84.A1S (EZXBASE_N_00.84.A1S_releasenote.txt)

BP: EZXBASE_G_10.46.B1I (EZXBASE_G_10.46.B1I_release_notes.html)

Flash tool:

RSDlite Tool: RSD 2.3 or higher should be used for flashing. It can be obtained here: http://compass.mot.com/go/rsdlite

Flash modes

- mbm ap mode: press VA/VR key (right side key) and power up the phone

- mbm bp mode: press VA/VR key (right side key) on power up and press VA/VR key a 2nd time

- blob ap mode: press left soft key on power up

When opening Windows “Device Manager”:

- If the mobile is enumerated as Motorola_NA_USBLAN , the IP address to access the AP file system is : 192.168.16.2

Table of contents

1.	Default flash procedure	3

1.1.	For BP	3

1.2.	For AP:	3

2.	1FF flash procedure	4

2.1.	AP boot replacement	4

2.2.	BP boot replacement	4

2.3.	BP Flex	4

2.4.	For 1FF	5

3.	Specific settings	7

3.1.	Motorola USB modem	7

3.2.	Test Command	7

3.3.	AP logger	7

3.4.	Test command and AP logger	7

3.5.	Setting DSM OFF	7

4.	How to activate the APR	8

5.	How to enable AP logging	9

6.	BP Erase procedure	10

6.1.	Backup Phasing	10

6.2.	Flash	10

6.3.	Flex	10

6.4.	Restore Phasing	10

# Default flash procedure

## For BP

### Flash

If the previous phone release is older than R57_G_10.06.3AI BP boot replacement is required, flash boot replacer as indicated below. If previous phone release is R57_G_10.06.3AI or above you just need to re-flash BP.

- Flash boot replacer

File name: A62_912_UA_10I_replacer_R57_G_10.06.A7I_hwcfg_block_flash.shx

- Reflash BP

File name: R57_G_10.07.05R_martinique_reflash.sbf

File location: http://compass.mot.com/go/155847489/R57/R57_G_10.07.05R/flash/MARTINIQUE/full

Flex

- Using Radiocomm, flex Manufacturing BP:

File name: GMZA9100000AA03E.hs

Flex location : http://gsm-web.pcs.mot.com/lca_releases/flex/GSM/R5.7/BP/03E/hs

- Using Radiocomm, flex Integration BP:

File name: GIZA9100000AA03C.hs

Flex location : http://gsm-web.pcs.mot.com/lca_releases/flex/GSM/R5.7/BP/03C/hs

- Using Radiocomm flex BP with for EDGE temperature compensation mechanism.

If these elements are not phased in factory, it is recommended to set default values to avoid EDGE Tx issues.

This element have been introduced since phone release R57_G_10.06.2AI (BP EZXBASE_G_10.2C.B1I)

Flex one of these two files:

  - bartinique_default_phasing_temperature_compensation.hs

  - bartinique_default_phasing_temperature_compensation.nvm

## For AP:

### Flash

In ap mbm mode, flash R57_G_10.07.05R_martinique_ap_full_reflash.sbf available at:

http://compass.mot.com/go/155847489/R57/R57_G_10.07.05R/flash/MARTINIQUE/full

Flex

Flex AP with Generic Core flex:

- Setup: GAC_GENERIC_GIZA910000GC_S040

- Secured setup: GAC_GENERIC_GCZA910000GC_E005

- Resource: GAC_GENERIC_GCZA910000GC_R57_G_10.07.05R_R001

# 1FF flash procedure

Depending on the SW version you have in your phone, please see below the steps to follow:

If the previous phone release is older than R57_G_10.06.3AI

Please follow 2.2/2.4

If the previous phone release is older than R57_G_10.06.38I:

Please follow 2.1/2.2/2.4

If the previous phone release is older than R57_G_10.06.2AI

Please follow 2.1/2.2/2.3/2.4

In all other cases : please follow only 2.4.

## AP boot replacement

If the previous phone release is older than R57_G_10.06.38I AP boot replacement is required, flash mbm as indicated below:

File name: R57_G_10.07.05R_martinique_mbm.sbf

File location: http://compass.mot.com/go/155847489/R57/R57_G_10.07.05R/flash/MARTINIQUE/ap_sbf

BP boot replacement

If the previous phone release is older than R57_G_10.06.3AI BP boot replacement is required, flash boot replacer as indicated below.

- Flash boot replacer

File name: A62_912_UA_10I_replacer_R57_G_10.06.A7I_hwcfg_block_flash.shx

## BP Flex

In addition of usual flex and phasing, other seem elements must be flexed (If not already flexed in phone)

- Using Radiocomm flex BP with for EDGE temperature compensation mechanism.

If these elements are not phased in factory, it is recommended to set default values to avoid EDGE Tx issues.

This element have been introduced since phone release R57_G_10.06.2AI (BP EZXBASE_G_10.2C.B1I)

Flex one of these two files:

  - bartinique_default_phasing_temperature_compensation.hs

  - bartinique_default_phasing_temperature_compensation.nvm

## For 1FF

1FFs are available at:

http://compass.mot.com/go/r571ff for non signed 1FF

or

http://compass.mot.com/go/r57signed1ff for signed 1FF

Starting from 10.06.40I we try to generate only signed 1FF.

In normal mode, flash your 1FF. If 1Ffis missing, please contact the owner mentioned in the table below.

You might see an issue using 1FF when phone does not enumerate in USB LAN LINK mode at power up. At the beginning of the flash procedure when RSD Lite forces your phone to go in ap mbm flash mode, your PC might report that your phone is not recognized any more. At this stage please unplug and plug back your USB cable. From there everything should go fine and RSD Lite should recover.

| Model | AP flex/Owner | Purpose | Setup | Secure Setup | BP Flex |
| --- | --- | --- | --- | --- | --- |
| Generic Core | GCZA910000GC (TLS Flex Team) | Core flex validation | S040 | E005 | GCZA910000AA |
| Standard integration | GIZA910STD01 (TLS Flex Team) | IPSEC ON, UMA ON, SS OFF | S054 | E020 | GIZA910000AA |
| Standard integration | GIZA910STD02 (TLS Flex Team) | Support Orange features | S036 | E019 | GIZA910000AA |
| Standard integration | GIZA910STD03 (TLS Flex Team) | FTA testing | S037 | E004 | GIZA910000AA |
| Standard integration | GIZA910STD04 (TLS Flex Team) | GNPO | S034 | E003 | GIZA910000AA |
| Toulouse integration | GIZA910TLS01 (TLS Flex Team) | Settings for all French customers | S080 | E005 | Not applicable |
| Cingular customer | GSZA910CIN05 (TLS Flex Team) | IOT Cingular | S033 | E003 | Not applicable |
| Tmobile customer | GSZA910TMB01 (TLS Flex Team) | IOT T-Mobile | S060 | E005 | Not applicable |
| EMEA core | GCZA910000AA (Anas Kaoukab) | Field Test EMEA |  | E004 | SE6826AXXZ9 |
| BT UK customer | GSZA910BTUK0 (Glen Marinus) | IOT BT |  | E006 | GSMA910BTUK |
| Orange France customer | GSZA910ORFR0 (Ulpha Parakala) | IOT Orange France |  | E008 | GSZA910BPORAFR |
| Orange Poland customer | GSZA910ORPL0 (Michal Kwiatkowski) | IOT Orange Poland |  | E005 | GCZA910BPORACOREEU |
| Orange UK customer | GSZA910ORUK0 (Charles Amoah) | IOT Orange UK |  | E009 | GCZA910BPORACOREEU |
| TELIA customer | GSZA910TELIA (Rickard Roberg) | IOT TELIA |  | E006 | SE6826AZ6Z9 |
| TIM Italy Customer | GSZA910TIMIT (Simone Ratti) | IOT TIM |  | E005 | GSZA910BPTIMIT |
| NA core | GCZA910000NA (Not maintenned) | Field Test NA |  | E003 | GCZA910000NA |

If you want to test specific configurations, please go to 3

# Specific settings

Full flex model list and history is available at:

http://easyflex-dev.ea.mot.com:8888/history.php?flx_product_id=1

| SEEM ELEMENT | DESCRIPTION | AP /BP | FLEX TYPE | CORE | CUSTOMER | INTEGRATION | COMMENTS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DL_DB_AP_TCMD | AP Test command | AP | SECURED | 0 | 0 | 1 | When set to ON will enable MTC mode MTC : Manual Test Command |
| DL_DB_AP_LOG_AVAILABLE | AP Logger | AP | SECURED | 0 | 0 | 1 |  |
| DL_DB_FEATURE_ID_USBNET | USB Net function | AP | SECURED | 0 | 0 | 1 | Controls "USB Net" display under Connections |
| None | USB Mode | AP | SETUP | Modem | Modem | Modem | Only taken into account when AP logger and Ap Test Command are both set to OFF |
| None | EFEM | BP | N/A | 0 | 0 |  |  |

## Motorola USB modem

- Secure setup: GAI_GENERIC_GIZA910STD01_E017

USB port will enumerate as Motorola USB modem

## Test Command

- Secured setup: GAI_GENERIC_GIZA910STD01_E018

USB port will enumerate as Motorola USBLan device.

## AP logger

- Secured Setup with AP logger: GAI_GENERIC_GIZA910STD01_E019

USB port will enumerate as Motorola USB device. This is for AP log capturing. You should be able to connect your phone with AP logger tool.

## Test command and AP logger

- Secured Setup with tcmd & AP logger: GAI_GENERIC_GIZA910STD01_E020

USB port will enumerate as Motorola USB device. This is for BP log capturing. You should be able to connect your phone with RTA tool.

Note: your phone's USB port will NOT enumerate as Motorola USB LAN device.

## Setting DSM OFF

- Using Radiocom, flex: DEEP_SLEEP_MODE_OFF.hs

# How to activate the APR

Flex the APR mini flex. Restart the phone.

You can retrieve the flexes from http://compass.mot.com/go/173938257

Note: All carriers should be able to use the EMEA mini-flex (SMS_+4477.hs). This will send Panic data in an SMS message to the system; however the number associated is a European number.  T-Mobile users can flash the T-Mob NA mini-flex (T_MOBILE_Email…hs).  The Cingular NA mini-flex should be available shortly.

# How to enable AP logging/telnet

Starting release R57_G_10.06.45I AP log/telnet have been turned off.

You can enable it by flashing the following sbf:

File Name: R57_G_10.07.05R_martinique_rootfs_cramfs_with_logging.sbf

File Location:

http://compass.mot.com/go/155847489/R57/R57_G_10.07.05R/flash/MARTINIQUE/ap_sbf

Note: The sbf does not contain any flexes, your specific settings will be kept. Because of image size limitation, WIFI Manufacturing drivers have been removed from this sbf.

You also need to flash a secure setup flex that enables AP log capturing. Refer to section 3 for more details.

# BP Erase procedure

## Backup Phasing

Backup phasing data using Radiocomm using file: bartinique_backup_template_ver3.nvm

## Flash

- In bp flash mode, blank the phone.

For P3 hardware, use Barbados/Martinique Eraser file.shx available at:

http://compass.mot.com/go/lte2%2Dbrickproof%2Derasers

Note: at the end of the flash, you have to switch on manually the mobile

- In bp flash mode, flash R57_G_10.07.05R_martinique_flash.sbf available at:

http://compass.mot.com/go/155847489/R57/R57_G_10.07.05R/flash/MARTINIQUE/full

## Flex

- Using Radiocomm, flex Manufacturing BP:

File name: GMZA910000AA03E.hs

Flex location: http://gsm-web.pcs.mot.com/lca_releases/flex/GSM/R5.7/BP/03E/hs

- Using Radiocomm, flex Integration BP:

File name : GIZA910000AA03C.hs

Flex location: http://gsm-web.pcs.mot.com/lca_releases/flex/GSM/R5.7/BP/03C/hs

- Using Radiocomm flex BP with for EDGE temperature compensation mechanism.

If these elements are not phased in factory, it is recommended to set default values to avoid EDGE Tx issues.

This element have been introduced since phone release R57_G_10.06.2AI (BP EZXBASE_G_10.2C.B1I)

Flex one of these two files:

  - bartinique_default_phasing_temperature_compensation.hs

  - bartinique_default_phasing_temperature_compensation.nvm

## Restore Phasing

Using Radiocomm, phase the phone with data that you backed up in step 6.1