# Motorola A920 3G Product Software Upgrade to A925 Procedure Notes

# December 12, 2003									Version 1.0b

FROM: Flash: Version (AP): 11.11 or 11.22 (A920 released versions)

Boot Loader: 01.01.46 – (POG based M02 Hardware)

NOTE: Software Version on A920 can be read by clicking Control Panel icon => Handset Information

TO: Flash: Version (AP): REL 21.58.01, Baseband (BP): A925_BP_21.58.00, AP Config: SA1141AXXW8_007A

## Flex: SA1109A00A

###### Boot Loader: 01.01.54

Needed files: Flash: REL_21.58.01_SA1141A_002_BP.shx Flex file: SA1141A00A.hs Boot-loader file: apb_tsh_010154.m0

NOTE: The new Software adds Bluetooth and other improvements, (i.e. allows 3rd party Symbian Software into handset, etc.) The phone should have the Boot Loader firmware upgraded, flashed, and then flexed following the below instructions.

##### Hardware Tools

## Pentium based PC with USB port with suitable memory to run MS Windows 2000 (SP3) or XP (SP1)

## Security WIBU Key – PC parallel port. Note: There are External and Internal version keys and most keys provided by Motorola are External versions. This procedure will discuss Flexing assuming that an External Key is used.

- USB Cable: SKN6311 (for flashing and flexing) AND RS232 Cable SKN6315 and Adapter SYN0279 (for Boot Loader programming)

- Power supply: SPN5049, A920 Phone battery with adequate charge (more than 1 bar on phone display)

##### Software Tools

1) For Boot Loader programming:

- Use Windows HyperTerminal application (Process on page 2)

2) For Flashing:

- MUST USE PST VERSION 6.2.1 or higher (Process on page 3)

3) For Flexing:

### MUST USE PST VERSION 6.2.1 Phone Programmer or higher or Radiocomm 6.4 or higher (Process on page 3)

Flashing and Flexing Notes:

Force flash mode (flashing only, and NOT flexing): Force flash mode simply speeds up the flashing process by forcing USB enumeration (detecting USB on computer and displaying small icon on PST Flash and test commands a bit faster saving you time). The phone can be flashed in Force Flash mode or NOT using Force Flash mode (powering up normally). Force Flash mode can be activated on the A920/925 by holding down both phone game buttons (at top of phone) and while inserting the USB cable plugged into the PC with the charger installed in the cable (battery not even needed). You will be able to read the Boot-Loader on the phone screen if Force Flash mode is activated correctly (black background with white letters)…

There are 2 options for flexing. To flex using PST Phone Programmer with External key you must create a new “3G Field Update File” and load flex file in that program, click the box, then run Field Update to start flexing process. Radiocomm Version 6.4 or higher is the fastest way to flex a phone, but the program may appear a bit more difficult to use for first time users. DO NOT USE the pFlex option in PST Phone Programmer to flex the A920 as it will result with a flex error. The pFlex option will only work with a Internal security key.  Flashing can also be done using the PST Phone Programmer option, but it is faster using PST Flash and Test command option.

USB Drivers (APPLIES TO FIRST TIME SET UP):

After loading Software Tools on the PC it will be necessary to power handset up with USB cable plugged in phone and PC and allow USB drivers to fully install on PC. This can initially takes a few power ups, and also note the phone may fail the flashing process the first time (do not panic) as the USB drivers continue to install (i.e. Installing special USB flash drivers as well as several others).

Customer Content

If the customer has unique content (i.e. pictures, phone numbers, ring-tones, etc.) not provided as factory default options on their A920 and want all this saved then it MAY be advisable to ask them to backup THEIR own CONTENT in the first instance. They have the ability to do all this themselves with the A920 Desktop Suite CD software provided in the phone kit by using the “archive option.” The other alternative is doing it for them. This process does not cover backing up A920 customer data – only doing the Software flash and Flex upgrade.  IMPORTANT NOTE: If you have the PST program and Radiocomm on the same PC as the A920 Desktop Suite program you may have to disable the M Router USB communication before using the PST or Radiocomm tool or a conflict will exist.

1) Boot Loader Programming:

Upgrading A920 Boot Loader from 01.01.4x to 01.01.54 (apb_tsh).

The Boot Loader version can be checked by putting the phone in Force Flash Mode using USB Cable and charger (battery not needed). However the Boot Loader must be programmed using the RS232 Cable and adapter, and Windows HyperTerminal application.

The step-by-step upgrade procedure for upgrading the Boot Loader is outlined below: 

1) Start the Hyper Terminal utility on your PC (Start/Programs/Accessories/Communications)

2) It must be set up for:

- The Serial COM port you connect the phone to. Then under "Configure"

- Bits per second: 115200

- Data bits: 8

- Parity: None

- Stop Bits: 1

- Flow Control: None

3) Connect the phone without a battery to your PC, using the straight through serial cable with adapter with the power connected to the CE connector while holding the 2 game buttons down. Once the cable is connected, release the games buttons.

4) On the HyperTerminal screen, you should see the list of options labeled 0 through 99 (not every number is in the list).  If you don't see the menu press RETURN.

5) Type 99 and hit Return (selecting option 99) - You should see CCCC... appearing in the HyperTerminal window

6) Click on Transfer

7) Click on Send File

8) Select the apb_tsh_010154.m0 file that is to be sent

9) Set Protocol to Xmodem

10) Click on Send

11) When the install is complete, approx. 1/2 minute, cycle power to the phone.

12) After power cycling the phone, verify the new boot loader version on the phones display by repeating step 3. IMPORTANT NOTE: CURRENTLY A MINOR GLITCH EXISTS WITH VERSION 01.01.54 IN NOT DISPLAYING THE BOOT LOADER SCREEN WITH A SERIAL CABLE AND YOU MUST VERIFY USING A USB CABLE.

13) Note that you can save the HyperTerminal session so you can recall the set up quickly for additional Boot Loader upgrades.

See attached Flashing and Flexing steps for the Motorola A920 (example screens shown)

# Text boxes

2) FLASHING (Using PST 6.2.1 Flash & Test Commands)

- Connect USB cable to PC and USB port and turn on phone (putting phone in force Flash mode is optional). Run PST Flash and Test Command option and load Flash file: REL_21.58.01_SA1141A_002_BP.shx

- Double click Motorola P2K icon (Blank A920 Paragon should appear in Platform Type box and Flash and Verify buttons should become black if loaded properly. “AP is on CE-Bus PST Connected” message should also appear on phones display (along with boot loader version – (bootloader on phone should be 01.01.46 or higher)

- Press Flash button – flashing successfully on a Pentium 4 computer should Complete in ~ 4 minutes (slower computers ~ 6+ minutes)

- Verify software version info in phone Control Panel  Icon=> Handset Information screen

3a) FLEXING (Using 6.2.1 PST Phone Programmer)

- Connect USB cable to PC and USB port and turn on phone. Run PST Phone Programmer (v6.2.1) Note – phone may power up prompting to choose Lang pack, and calibrate screen (choose English, and follow display calibration instructions until complete (phone should restart to normal power up screen when complete.

- Click on “File” and select  “New” and select “3G Field Update File”.

- Click on “Untitled Flex file” to load flex file: SA1141A00A.hs and select flex option box.

- To Flex phone press “Field Update” button.

- Flexing should take <3 minutes to complete

- Perform Master Reset and Clear through phone menu. Calibrate screen again if needed again.

- Verify software version and flex info in phone Control Panel  Icon=> Handset Information screen

- Complete

3b) FLEXING (Using Radiocomm version 6.4)

- Connect USB cable to PC and USB port and turn on phone. Run Radiocomm. Note – phone may power up prompting to choose Lang pack, and calibrate screen (choose English, and follow display calibration instructions until complete (phone should restart to normal power up screen when complete.

- Select “Main”,  “MA” and “3G” on Radiocomm

- Select “3G2” tab

- Select “Settings”, then “USB”, then “USB Settings > Initialize”

- Click on SUSPEND button and command will be sent to the phone – Green indicates that the command is sent SUCESSFULLY

- Browse to FLEX box and Load the flex file: SA1141A00A.hs

- Press the FLEX button. Flexing should complete in < 1 minute.

- Locate INVM section and initiate Master CLEAR (wait for command to complete successfully) and then initiate Master RESET

- Verify software version and flex info in phone Control Panel  Icon=> Handset Information screen

- Complete

NOTE: “USB Initialized” indicator after step 4 or green USB ready light indicates proper connection. Step 4 & 5 not needed if green USB ready light is on immediately