Canary

GSM Mid-Tier

Iconic Program

Product Description

Version 1.1

Product Line Management Lead

Bill Kastritis

Global Marketing

Tim Gassmere

Engineering

Mike Spence - ME

Dave Priniski - EE

SW -

Program Manager

Kevin Ray

Business Manager

Pam Spain

Using this Template

Any product created must be competitive within its market conditions. This document is a way to capture those specific competitive requirements and track PCS’s ability to meet them for a given time frame.

The “Required” column that appears in all tables throughout this document is used to indicate the specific requirement requested from Marketing.

The columns labeled “Commit” refer to engineering’s level of commitment to that specific feature in the product design.

To help manage feature creep, the following priority levels will be assigned to certain product attributes:

ESSENTIAL – the product must include all of these attributes to be successful toward its mission

IMPORTANT – these attributes are highly desirable, though no single one of them can be labeled “essential”.  Some subset (one to two thirds) of these attributes must be included in the product commitment. The exact mix is subject to flexible negotiations between marketing and engineering, but it is unacceptable for engineering to ignore these attributes and commit to only the essential list.

OPTIONAL – these attributes should be seriously evaluated for feasibility, but if none can be included due to unacceptable trade-offs in high priority areas, the product concept is still viable, albeit with an altered marketing strategy.

Requirements such as launch date and product costs are shown as numerical targets, and may indicate a range between “optimal” and “acceptable”.

Do not change the name or order of the sections or sub-sections in this template. All Product Description documents will be constructed the same way to minimize bias and maximize rigor. Individual tables can be modified to reflect the specific needs of your program. If additional information is required that is not covered in this template, add it to the end of the document.

Every Product Description document will have an associated Business Case document. When asked, place a link and indicate the location of that document for others to reference when needed.

Revision History

| Doc Revision | Date Changed | Name | Modifications Made |
| --- | --- | --- | --- |
| 1.0 | May 9, 2005 | Bill Kastritis | Initial Release |
| 1.1 | June 3, 2005 | Tim Gassmere | Updated the following sections: Hardware, Accessories, SW features and customization, competitive set |
| 1.2 | June 8, 2005 | Tim Gassmere | Updated the SW requirement link, Accessories and phone thickness |

Table of Contents

1.	Product Overview	5

1.1.	Summary of Value Proposition and Key Selling Points	5

1.2.	Competitive Differentiators	7

1.3.	Business Case Document –	9

2.	Product Variations and Cost Summary	9

2.1.	Product Variations and Launch Dates	9

2.2.	Manufacturing Costs (MCPU)	9

3.	Hardware Requirements	9

3.1.	Air Interface Standards	9

3.2.	Integrated Circuits	10

3.3.	Transceiver Performance	10

3.4.	RF and SAR Issues	12

3.5.	Digital Talk and Standby Times	12

3.6.	Analog Talk and Standby Times (N/A)	12

3.7.	Average Daily Usage by Consumer	12

3.8.	Battery Charge Times (to 90% Capacity)	12

3.9.	Mechanical Requirements	14

Camera Specifications	17

4.	Form Factor	17

4.1.	Industrial Design	17

4.2.	Hardware Customization (Postponement and Co-Branding)	18

4.3	Colors, Finishes, Graphics and Placement –	18

5.	Embedded Software Features and User Interface	18

5.1.	OS Support/Release/Feature List	18

5.2.	End User Memory Calculations	19

5.3.	Data Support	19

5.4.	Carrier Flex Requirements	19

5.5.	Languages Supported	20

5.6.	SIM Lock Options List	21

5.7.	Embedded Software Customization (Postponement and Co-Branding)	21

6.	Compliance and Regulations	22

6.1.	Government Regulations and Constraints	22

6.2.	Other Regulations and Constraints	23

6.3.	Infrastructure Compliance	23

6.4.	Disability Compatibility	23

7.	Accessories and Connectivity	27

7.1.	Packaged with Product	27

7.2.	After Market (Necessary and Optional)	28

7.3.	Connectivity	28

8.	Downloadable Applications and Services	28

8.1.	Programs, Content, and Services	28

8.2.	Standards and Compatibility for Downloads	29

9.	Distribution Strategy	29

9.1.	External Name	29

9.2.	Labeling Requirements	29

9.3.	Manual Requirements	29

9.4.	Product Variations and Box Contents	29

9.5.	New Sales Models	30

# Product Overview

Mobile Devices Business has enjoyed great success with Razor in 2004 and expects big things from Pebl and Slvr in 2005.  In 2006 we look to continue that trend with the introduction of the next icon internally named Canary.

During the initial product conception Canary was thought to be a lower cost refresh to Razr.  After further evaluation of consumer preferences and competitive landscape, the direction of the program has evolved to be a very compelling iconic product offering.

Canary features will include:

- 2 Mega-pixel camera

- Moto Sync – Over the air synchronization of contacts, calendar and email

- T-Flash external memory

- i-Tunes client with airplane mode and stereo EMU

- Dynamic Idle

- VST

- Full 262K (18 bit) color wallpapers & screensavers

- 65K color external display

- Class 12 EDGE

A brief description of the Canary target consumer:

- They purchase high priced, inaccessible luxury items

- They insist on being connected to the best of everything.

- They have a very strong desire to be seen as connoisseur of quality.

- They look for authenticity, consistency and product integrity.

- For them appreciation for the best verges on obsession.

## Summary of Value Proposition and Key Selling Points

The Canary Essence:

Where slender and thin become one

Value Proposition

The Motorola Canary achieves the trifecta in mobile devices by perfectly balancing Design, Craftsmanship and Functionality all in a stunningly slim package.

Key Selling Points/Consumer Experience:

A legend reborn –

Building upon one of the most celebrated design of the past decade, the Canary product delivers a new and exciting design experience utilizing exquisite materials and finishes.

Ultimate Imaging –

Take advantage of the 2 Mega pixel camera, video capture and memory card storage to capture every key moment in high definition.

Synchronization made easy –

Synchronize all of your contacts, calendar and email over the air at the click of a button utilizing the new Moto Sync application.

Take your music with you–

i-Tunes™ music player, T-flash memory, and airplane mode give you music and mobile to go.  (MP3 player all for regions where i-Tunes is not available)

Key Selling Points/Operator Experience:

Bigger and better ARPU –

Moto Sync, 2 Mega pixel camera, memory card and video capture mean more data, more often.

One key press–

Dedicated operator key keeps your portal front & center.

EDGE –

Consumers enjoy even faster browsing, modem, and data transfer, while you enjoy the bandwidth savings and increased revenue.

No more Idle time–

Dynamic Portal support delivers customized content for each user.  A non-intrusive way to drive revenue and lock in consumers with unique and personalized services.

## Competitive Differentiators

Summary:

Canary has an EDGE regarding:		Canary is competitive regarding:

Design and CMF					Edge/GPRS

Smallest 2 MP camera phone in the world	VST

Quad Band internal antenna			Internal and removable memory

Over the air synchronization			Internal & external displays

i-Tunes & Stereo support

### Competitive Benchmarking

Products focused on Style and Design

2 Mega Pixel Camera Phones

Canary Competitive Summary:

Vanta g	Competition is better

Canary is equivalent

Red: Di	 Canary is better

See details on competitive products on compass site below.

http://wiser-emea.mot.com

http://bi.mot.com/

## Business Case Document –

Due to the Motorola Confidential information disclosed in the Business Case, please access the full document located at the Compass site below.

http://compass.mot.com/go/159743988

The top customers for this program are:

# Product Variations and Cost Summary

## Product Variations and Launch Dates

Canary will only be available in one color.

| Parameter | Comments | Required | Commit |
| --- | --- | --- | --- |
| GPRS Quadband | N. Asia | Q1 2006 |  |
| GPRS Quadband | High Growth Markets | Q2 2006 |  |
| GPRS Quadband | Europe | Q1 2006 |  |
| GPRS Quadband | North America | Q2 2006 |  |
| GPRS Quadband | Latin America | Q2 2006 |  |

## Manufacturing Costs (MCPU)

Due to the sensitivity of the Manufacturing Costs, please access this information at the Compass site below:

(permission needed for access)

http://compass.mot.com/go/159743988

# Hardware Requirements

The Canary Hardware Requirements can be found at the following Compass site below:

(permission needed for access)

http://compass.mot.com/go/159743988

# Form Factor

## Industrial Design

Canary is in the process of being locked down.  Post lockdown, the ID will not be included within this PD in order to maintain the confidentiality of the design.  The ID will be shared with Regions per Mobile Devices on an as needed basis.

One color will be available at launch.

## Hardware Customization (Postponement and Co-Branding)

| Parameter | Comments | Required | Commit |
| --- | --- | --- | --- |
| Housing (external) color (flip and battery door) | One color at SA | Essential |  |
| Chassis color (internal Mag parts & ski-slope) | One color at SA | Essential |  |
| Keypad | 7 STD languages | Essential |  |
| Escutcheon Label | Co-brand will be done on battery door | Not required |  |
| Battery door Labeling | Laser etching or Printing. Printing limited to 2 colors | Essential |  |

Carrier logos and physical co-branding will be achieved by laser etching on battery door.  This will be the only co-branding location and will be available for customers 100K Units or more for 2006.  Carrier logos may appear in the display itself as part of a power up banner, wallpaper, screensaver or splash screen.

## Colors, Finishes, Graphics and Placement –

| Parameter | Comments | Required | Commit |
| --- | --- | --- | --- |
| External CLI Lens | Motorola Logo in Lens | Essential |  |
| Internal Lens | Motorola logo at top of lens | Essential |  |
| Battery door | Motorola Batwing on battery door | Essential |  |

# Embedded Software Features and User Interface

## OS Support/Release/Feature List

Canary release R4.52.7 will be based off of the P5.2 platform, below is the link to the Canary SW list and link to the FMDB. *For the latest Canary feature status please see the FMDB

http://compass.mot.com/go/159743988

The specific Canary release can be found on the Feature Management Database:

http://features.pcs.mot.com/

## End User Memory Calculations

The end user memory calculator can be found at the following compass site:

http://compass.mot.com/go/128765643

## Data Support

| Feature | Comments | Required | Commit | MRS # |
| --- | --- | --- | --- | --- |
| GPRS Class 12 |  | Essential | Yes | In Baseline |
| Phase II USSD |  | Essential | Yes | In Baseline |
| High Speed circuit switch data |  | Not required | No | N/A |
| CSD - Up to 14.4Kbps standard data operation |  | Essential | Yes | In Baseline |
| IrDA support |  | Not Required | No | N/A |
| Phone book sync (Mobile Phone Sync) |  | Essential | Yes | In Baseline |
| EDGE Class 12 |  | Essential | Yes | 10134 |
| Bluetooth (Class 2) |  | Essential | Yes | In Baseline |
| USB Cable support |  | Essential | Yes | In Baseline |

## Carrier Flex Requirements

Please Note:  A core flex will be generated by the core product team for generic settings.  The regions will own responsibility to create customer and regional specific flex requests via VRF’s (Variant Request Forms).

## Languages Supported

| Language | Prompts | MT-SMS CB SMS | Multi-Tap Input Phonebook | Multi-Tap Input MO-SMS | Multi-Tap Input WAP | iTap Input Phonebook | iTap Input MO-SMS | iTap Input WAP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Arabic | ( | ( | ( | ( | ( | ( | ( | ( |
| Bahasa Indonesia | ( | ( | ( | ( | ( | ( | ( | ( |
| Bahasa Malay | ( | ( | ( | ( | ( | ( | ( | ( |
| Bulgarian | ( | ( | ( | ( | ( | ( | ( | ( |
| Croatian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Czech | ( | ( | ( | ( | ( | ( | ( | ( |
| Danish | ( | ( | ( | ( | ( | ( | ( | ( |
| Dutch | ( | ( | ( | ( | ( | ( | ( | ( |
| English American and UK | ( | ( | ( | ( | ( | ( | ( | ( |
| Estonian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Finnish | ( | ( | ( | ( | ( | ( | ( | ( |
| French | ( | ( | ( | ( | ( | ( | ( | ( |
| French Canadian | ( | ( | ( | ( | ( | ( | ( | ( |
| German | ( | ( | ( | ( | ( | ( | ( | ( |
| Greek | ( | ( | ( | ( | ( | ( | ( | ( |
| Hebrew | ( | ( | ( | ( | ( | ( | ( | ( |
| Hindi | ( | ( | ( | ( | ( | ( | ( | ( |
| Hungarian | ( | ( | ( | ( | ( | ( | ( | ( |
| Italian | ( | ( | ( | ( | ( | ( | ( | ( |
| Latvian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| LA Spanish (Colombian) | ( | ( | ( | ( | ( | ( | ( | ( |
| LA Portuguese (Brazilian) | ( | ( | ( | ( | ( | ( | ( | ( |
| Lithuanian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Norwegian | ( | ( | ( | ( | ( | ( | ( | ( |
| Polish | ( | ( | ( | ( | ( | ( | ( | ( |
| Portuguese | ( | ( | ( | ( | ( | ( | ( | ( |
| Romanian | ( | ( | ( | ( | ( | ( | ( | ( |
| Russian | ( | ( | ( | ( | ( | ( | ( | ( |
| Serbian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Slovak | ( | ( | ( | ( | ( | ( | ( | ( |
| Slovenian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Spanish | ( | ( | ( | ( | ( | ( | ( | ( |
| Swedish | ( | ( | ( | ( | ( | ( | ( | ( |
| Tagalog | ( | ( | ( | ( | ( | ( | ( | ( |
| Thai | ( | ( | ( | ( | ( | ( | ( | ( |
| Traditional Chinese | ( | ( | ( | ( | ( | ( | ( | ( |
| Simple Chinese | ( | ( | ( | ( | ( | ( | ( | ( |
| Turkish | ( | ( | ( | ( | ( | ( | ( | ( |
| Ukrainian | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Vietnamese | ( | ( | ( | ( | ( | ---- | ---- | ---- |
| Urdi / Farsi | ( | ( | ( | ( | ( | ---- | ---- | ---- |

## SIM Lock Options List

| SIM Lock Type |  |
| --- | --- |
|  | Priority | Commit | Comment |
| HPLM Only | Essential |  |  |
| Type 1 HPLMN and 1 IMSI digit | Essential |  |  |
| Type 2 HPLMN and 2 IMSI digits | Essential |  |  |
| Type 3 HPLMN and GID 1 | Essential |  |  |
| Type 4 HPLMN and Range of IMSI digits | Essential |  |  |
| Type 5 First SIM Inserted | Essential |  |  |
| Type 6 First SIS Inserted (GID 1 or No action) | Essential |  |  |
| Type 7 First SIM Inserted (GID 1 or Range Setting) | Essential |  |  |
| Type 9 PLMN of first SIM Inserted | Essential |  |  |
| D2 SIM Lock | Essential |  |  |
| Philippines (HPLMN that matches 1st SIM Inserted) | Essential |  |  |
| Valid PLMN | Essential |  |  |
| Telefonica SIM Lock | Essential |  |  |
| Airtel SIM Lock | Essential |  |  |

## Embedded Software Customization (Postponement and Co-Branding)

Unique Skinning will be made available based on a minimum order quantity.   These will be reviewed with the Product Core team.

# Compliance and Regulations

## Government Regulations and Constraints

| Approvals | Comments | <GSM> |
| --- | --- | --- |
|  |  | Required | Commit |
| North America: |  |  |  |
| FCC+Canada | EOTD req for NA | Yes | Yes |
| Standard European: |  | Yes | Yes |
| Russia | TBD by region | Yes | Yes |
| Ukraine | TBD by region | Yes | Yes |
| Hungary | TBD by region | Yes | Yes |
| Czech Republic | TBD by region | Yes | Yes |
| Israel | TBD by region | Yes | Yes |
| Slovak Republic | TBD by region | Yes | Yes |
| Poland | TBD by region | Yes | Yes |
| Latin America | TBD by region | Yes | Yes |
| Asia: | TBD by region | Yes | Yes |
| China |  | Yes | Yes |
| Hong Kong |  | Yes | Yes |
| Taiwan |  | Yes | Yes |
| Thailand |  | Yes | Yes |
| Australia |  | Yes | Yes |
| Singapore |  | Yes | Yes |
| Malaysia |  | Yes | Yes |
| Indonesia |  | Yes | Yes |
| Philippines |  | Yes | Yes |
| New Zealand |  | Yes | Yes |

## Other Regulations and Constraints

| Approvals | Comments | <GSM> |
| --- | --- | --- |
|  |  | Required | Commit |
| UL | Accessories only | Yes | Yes |
| CTIA |  | Yes | Yes |
| BABT |  | Yes | Yes |

## Infrastructure Compliance

| Infrastructure | <GSM> |
| --- | --- |
|  | Required | Commit |
| Ericsson | Yes | Yes |
| Motorola | Yes | Yes |
| Alcatel | Yes | Yes |
| Siemens | Yes | Yes |
| Nokia | Yes | Yes |
| Lucent | Yes | Yes |
| Nortel | Yes | Yes |
| ShangHai Bell | Yes | Yes |
| ZTE | Yes | Yes |
| Samsung | Yes | Yes |
| Hua Wei | Yes | Yes |

## Disability Compatibility

The DA feature tracking for Canary is attached below.

| PRODUCT | Canary |
| --- | --- |
| PS&C REFERENCE # |  |
| THUMBNAIL IMAGE | N/A |
| SIGNALING | GSM 850, 900, 1800, 1900 |
| U.S. PRODUCT | Yes |
| SA STATUS | Q1 2006 |
| HEARING / SPEECH RELATED FEATURES These features tend to increase the usability of the product for people who have limited hearing and/or speech capabilities. | FEATURE STATUS COMMITTED = Development Commitment NO = Not On the Product N/A = Not Applicable to the Product VERIFIED = Feature Verified by PS&C |
| Expected Basic Features |  |
| Vibracall Alert | COMMITTED |
| Visual Alerts for Power-On, Power-Off, and Low Battery | COMMITTED |
| Keypad Depression Feedback (visual and/or tactile) | COMMITTED |
| Hearing Aid Coupling Speaker (e.g., dynamic speaker) | COMMITTED |
| Standard 2.5 mm Headset Jack / Audio Cut-off | COMMITTED As an Accessory with a Dongle via the EMU connecctor |
| Motorola Neckloop Compatible (SYN7875) | COMMITTED As an Accessory with a Dongle via the EMU connecctor |
| TTY Compatibility (carrier dependent) | COMMITTED As an Accessory with a Dongle via the EMU connecctor |
| Additional Features |  |
| Variety of Ringer Tones over various frequency ranges | COMMITTED |
| Connectivity to Augmentative Speech Device | NO |
| Two-Way Text Messaging | COMMITTED |
| Speech-to-Text Feature (user's words converted to text) | NO |
| Concave "cupped" earpiece housing | NO |
| Additional accessories that could improve hearing / speech accessibility: | NO |
| Other Hearing/Speech Related Features: | NO |
| VISION RELATED FEATURES These features tend to increase the usability of the product for people who have limited visual capabilities. | FEATURE STATUS COMMITTED = Development Commitment NO = Not On the Product N/A = Not Applicable to the Product VERIFIED = Feature Verified by PS&C |
| Expected Basic Features |  |
| Nib on 5 Key and/or Nibs on F and J keys (QWERTY) | Raised surface Around the 5 Key COMMITTED |
| Keys are “raised” from surface and can be distinguished by touch | COMMITTED |
| Function keys look and feel different from Number Keys | COMMITTED |
| Keypad Depression Feedback (audible and/or tactile) | COMMITTED |
| Unique Sounds for both Power-On and Power-Off | COMMITTED |
| Distinct Sounds for Function keys versus Number keys | COMMITTED |
| Audible Low Battery Warning | COMMITTED |
| Audible Volume Level Indicator | COMMITTED |
| Display Backlighting | COMMITTED |
| Colorblind Friendly (Color is not be the only means of conveying information) | COMMITTED |
| Alternate Format User Manuals | COMMITTED |
| Additional Features |  |
| Ringer I.D. for identifying callers | COMMITTED |
| Voice Dialing | COMMITTED |
| Voice Menu Navigation | COMMITTED |
| Display information is spoken by the product | NO |
| Menus are spoken by the product | NO |
| Speech-to-Text Feature (user's words converted to text) | NO |
| Voice Recorder | COMMITTED |
| Global Positioning System (GPS or AGPS) | NO |
| Backlight for Keypad (keys visible in the dark…) | COMMITTED |
| Zoom display or Enlarged Fonts | COMMITTED |
| Adjustable Contrast Display | COMMITTED |
| Common Symbols / Icons for explanations | COMMITTED |
| Plug Polarity (User can not plug in the wrong way) | COMMITTED |
| External, "snap-in" battery (N/A for embedded batteries) | COMMITTED |
| Additional accessories that could improve vision accessibility: | NO |
| Other Vision Related Features: | NO |
| MOVEMENT / MANIPULATION RELATED FEATURES These features tend to increase the usability of the product for people who have limited movement and/or manipulation capabilities. | FEATURE STATUS COMMITTED = Development Commitment NO = Not On the Product N/A = Not Applicable to the Product VERIFIED = Feature Verified by PS&C |
| Expected Basic Features |  |
| Total Weight Less than 12 oz (340g) | COMMITTED |
| Shape of Device (e.g., "Candy Bar" / "Clam Shell"): | CLAM SHELL |
| Side Indents / Tabs for Flips | COMMITTED |
| Touch Screens: Not Heat Activated (Human touch not required to activate touch screen) | N/A |
| Keypad Depression Feedback (audible and/or visual) | COMMITTED |
| Additional Features |  |
| Lanyard Pin for key ring or wrist strap | COMMITTED |
| iTAP capable | COMMITTED |
| Optional mode if multiple keys must be depressed simultaneously | NO |
| Menu actions either reversible or able to have request for confirmation (e.g., “Undo” or “Are you sure?”) | COMMITTED |
| No controls that require pinching, twisting, or wrist rotation | COMMITTED |
| Buttons/keys have non-slick surface | NO |
| “Automatic Answer” feature | COMMITTED |
| “Any Key Answer” feature | COMMITTED |
| External, "snap-in" battery (does not apply to embedded batteries) | COMMITTED |
| Non-slip grips on sides of product | NO |
| Flat back on product for table-top operation | COMMITTED |
| Speech-to-Text Feature (user's words converted to text) | NO |
| Auto-redial feature when system is busy | COMMITTED |
| Additional accessories that could improve Movement / Manipulation accessibility: | NO |
| Other Movement / Manipulation Related Features: | NO |
| COGNITION / OTHER RELATED FEATURES These features tend to increase the usability of the product for people who have limited cognitive capabilities or other disabilities not specifically covered by the above categories. | FEATURE STATUS COMMITTED = Development Commitment NO = Not On the Product N/A = Not Applicable to the Product VERIFIED = Feature Verified by PS&C |
| Expected Basic Features |  |
| Function keys look and feel different from Number Keys | COMMITTED |
| Similar Functions Grouped Together | COMMITTED |
| Manual Scroll Operation (User scrolls through messages at own pace) | COMMITTED |
| Screen Refresh outside of 3 Hz and 60 Hz range (reduce "flicker") | COMMITTED |
| Additional Features |  |
| User Responses Independent of Time Limits | COMMITTED |
| iTAP capable | COMMITTED |
| Common Symbols / Icons for explanations | COMMITTED |
| Auto-redial feature when system is busy | COMMITTED |
| “Automatic Answer” feature | COMMITTED |
| Lanyard Pin for key ring or wrist strap | COMMITTED |
| Menu actions either reversible or able to have request for confirmation (e.g., “Undo” or “Are you sure?”) | COMMITTED |
| “Any Key Answer” feature | COMMITTED |
| Voice Dialing | COMMITTED |
| Voice Menu Navigation | COMMITTED |
| Display information is spoken by the product | NO |
| Menus are spoken by the product | NO |
| Speech-to-Text Feature (user's words converted to text) | NO |
| Voice Recorder | COMMITTED |
| Global Positioning System (GPS) | NO |
| Plug Polarity (User can not plug in the wrong way) | COMMITTED |
| External, "snap-in" battery (does not apply to embedded batteries) | COMMITTED |
| Additional accessories that could improve Cognition / Other accessibility: | NO |
| Other Cognition / Other Related Features: | NO |

# Accessories and Connectivity

| Accessories | Comments | Required | Commit |
| --- | --- | --- | --- |
| 740 Nominal Battery |  | Essential |  |
| Bluetooth Pro Car Kit |  | Essential |  |
| Bluetooth Headset (Mini Blue) H5 |  | Essential |  |
| Bluetooth PC USB Adapter | SYN0717A | Important |  |
| EMU – VPA |  | Essential |  |
| EMU - Mono Send-End Headset |  | Essential |  |
| EMU - Stereo Send-End Headset |  | Essential |  |
| EMU - Travel Chargers | Current portfolio | Essential |  |
| EMU-Rapid Charger (US/UK/EMEA) |  | Essential |  |
| EMU - Self Install Car kit |  | Essential |  |
| EMU - Mini USB Data Cable | SKN6371 | Essential |  |
| Mobile Phone Tools (MPT) Phase III - USB Cable + MPT (bulk) - MPT CD-ROM only (bulk) - MPT CD-ROM only (white box) |  | Essential |  |
| Leather Case |  | Essential |  |
| Belt Clip | SYN9766B | Essential |  |
| Right Angle Dongle for Charging |  | Essential |  |
| Trans Flash Card |  | Essential |  |
| Trans Flash – SD adapter |  | Essential |  |
| Next Generation RAZR Wire |  | Nice to have | Not committed from CPAD |

Please note:  The Excel Worksheet below is the accessory portfolio for Canary.  This accessory portfolio matrix will be re-freshed based on new accessory availability.

http://compass.mot.com/go/159739481

## Packaged with Product

| Accessories | Comments | Required | Commit |
| --- | --- | --- | --- |
| EMU Switching Travel Charger |  | Yes | Yes |
| Manual |  | Yes | Yes |
| 740 Nominal Battery |  | Yes | Yes |
| Battery Door |  | Yes | Yes |
| Trans Flash Card | Cost estimates do not currently include a trans-flash card in box | TBD | NA |
| EMU - Stereo Send-End Headset | Cost estimates do not currently include a headset in box | TBD | NA |

Please note:  Anything, such as those items listed below, above the standard package will require additional cost and revenue justification by the regions.

## After Market (Necessary and Optional)

See the above, section 7, chart for after market accessories

## Connectivity

| Connectors needed | Comments | Required | Commit |
| --- | --- | --- | --- |
| EMU Mini-USB |  | Yes |  |
| External RF for CarKit |  | N/A |  |
| External RF for Carrier Testing |  | Yes |  |

# Downloadable Applications and Services

[This section is to ensure that we are identifying all of the content and required services to create the most compelling experience for this concept.].

## Programs, Content, and Services

The preloaded media (screensavers, wallpapers, ringtones, etc) will compliment the overall product proposition and moto-zone, motochic.  The Product team will be working with the various Regions to lock the content down for this product.  Please note that we have allocated 4MB in the memory calculator to be used for all the preloaded media, games and apps, similar to the Santorini and Fiji programs.

http://compass.mot.com/go/motochic

Specific media, games and apps to be preloaded on Canary will be decided upon after M11.

Note: preloading of any operator provided media will require a liability waiver be completed PRIOR TO the incorporation of said media into a flex file.  Additionally, ring tones must be tested & optimized on the Canary hardware. If the tones do not meet audio specifications, they will require a department number to charge for the optimization.

## Standards and Compatibility for Downloads

| Description | Comments | Required | Commit |
| --- | --- | --- | --- |
| Full support of J2ME OTA Download |  | Essential | Yes |
| SSL 3.0 or later version |  | Essential | Yes |
| TLS – Latest version |  | Essential | Yes |
| MMS |  |  |  |
| Full MMS – SMIL as supported in the MMS 2.0 conformance document |  | Essential | Yes |
| Sync (Local & OTA) |  | Essential | Yes |
| J2ME APIs and VSCL (Vodafone) |  | Essential | Yes-MIDP 2.0 |

# Distribution Strategy

## External Name

The external name will be provided by the nomenclature team after M11 approval.

## Labeling Requirements

| Parameter | Comments | Required | Commit |
| --- | --- | --- | --- |
| Sales model label |  | Yes |  |
| Box-bar code |  | Yes |  |
| Transceiver label |  | Yes |  |
| Battery label |  | Yes |  |
| CE distribution label |  | Yes |  |
| Escutcheon Co-Branding |  | Yes |  |
| Factory Label |  | Yes |  |
| Static Cling on Display |  | Yes |  |

## Manual Requirements

| Market | Manual Kit | Warranty + Reg. | Required | Commit |
| --- | --- | --- | --- | --- |
| Motorola Generic |  |  | Yes |  |

A generic manual in US English will be produced by ITC in conjunction with Core Product Marketing.  All other variants will be the responsibility of regional localization teams.

## Product Variations and Box Contents

Please see section 7 for the available accessories planned for Canary.

## New Sales Models

[How many and what types of models are needed at launch]

| Parameter | Comments | Required | Commit |
| --- | --- | --- | --- |