Motorola One

Trouble Shooting Guild

LENOVO

Contents

1.	Assembly and disassembly guide	3

1.1	Disassembly guide	3

1.2	Assembly guide	17

2.	PCBA layout	17

2.1	TOP	17

2.2	18

3.	analysis and elimination of common failures of flow	19

3.1	no power on	20

3.2	CTP problem	21

3.3	No  display	24

3.4	dead	26

3.5	NO key	27

3.6	Bad display screen	28

3.7	NO SPK	29

3.8	small bell	29

3.9	No charge	31

3.10	Can't take pictures	32

3.11	Automatic shutdown	32

3.12	The board leakage	34

Assembly and disassembly guide

## Disassembly guide

Tools：Retrieve card pin, cross screwdriver , tweezers, Plastic sheet, sucker

- Remove SIM card tray.

- Remove battery cover

2.1 Heat the battery cover in red box area with the hot air gun.

2.2 Draw a battery cover from the bottom of the cell with a sucker. To open the battery cover a gap, and then disassemble the battery cover open scribing.

Note: when the battery cover is dismantled, you need to press the fingerprint module with the top of the finger to separate the lid from the battery cover and then disassemble the battery cover. The following diagram

- Remove screws, fingerprint module and rear cover

3.1  Remove 1 black screws of the fixe connector compaction steel sheet, and remove the connector compaction steel sheet. Then disassembly the fingerprint reader connector.

3.2 the screws of the rear shell and the antenna support are disassembled with the cross screwdriver.

3.3 Disassembly the rear cover cooling film from battery.

3.4 Remove the rear cover, Then disconnect the battery connector.

- Remove PCBA.

4.1 Remove the key FPC connector Mylar.

4.2 The LCD and the TP interface, the main FPC interface, the key FPC interface and the RF cable interface are disassembled, and then the 2 main board screws are removed.

4.3 Remove the main board from three in one.

- Remove the earphone jack rubber sleeve.

- Remove the RGB led and light sensor rubber sleeve.

- Remove the rear camera and front camera from the main PCBA.

Note: After disconnecting the front camera connector, be careful to remove the copper foil from the front camera and prevent damage.

- Remove the receiver and flash light rubber sleeve from the front cover.

- Remove the 6 black screws,then remove the speaker box.

- Disassemble the main FPC connector and RF cable connector. Then disassembly the sub PCBA from the upper left part of sub PCBA and remove the sub PCBA from the front cover.

- Remove the vibrator.

- Remove the main MIC rubber sleeve.

- Remove the residual glue of battery cover. Then remove the RF cable.

- Pull out the easy to pull glue of  the fixed battery. Then remove the battery.

Note: Be very careful when remove the battery. To prevent damage to the battery.

- Remove the main FPC.

- Remove receiver ,light senser cap and Maim MIC cap

## Assembly guide

The handset is installed in reverse  order to removal.

。

# PCBA layout

## TOP

## Bottom

SUB PCBA TOP

SUB PCBA bottom

# analysis and elimination of common failures of flow

Requirement description:

Fault a fault is a customer call top10;

Fault diagnosis from the changing parts repair into the componentrepair;

To determine which device damage caused

The need to provide quick check method of the device is damaged

## no power on

## CTP problem

### Charging anomaly

### The charger is plugged in, without charging display

### Insert the USB line, the port was not found in thecomputer

## No  display

### No display

### LCD NO back light

## dead

## NO key

## Bad display screen

## NO SPK

## small bell

## No charge

## Can't take pictures

## Automatic shutdown

## The board leakage

# Text boxes

Retrieve card pin

SIM and TF  card tray

sucker

Press the fingerprint module on the belly of the finger and separate it from the battery cover

The fingerprint module has been separated from the battery cover

Battery cover

Press steel sheet

fingerprint module

Rear cover

Key connector Mylar

2 screws

Key FPC conn.

LCD&TP conn.

Main FPC conn.

RF cable conn.

PCBA (main board)

Re welding or replace PMIC

Check the PMIC main power supply is normal or not?

N

No power on

Check the 19.2MHz crystal is normal?

N

Y

Re welding

Single board with the power to the mobile phone power on whether there is a large current?

N

Y

The motherboard is damaged, replace the motherboard,fault plate gradually

N

Check the 32KHz crystal is normal? Whether the 32KHzsignal?

Y

Check the battery connector welding normal?

Y

N

Re welding

Re welding

N

Check whether the power button FPC assembly is good? Change theboot key FPC?

Y

Such as the replacement of the FPCB OK, is FPCB bad。

Connected to the computer through the USB line, check the computer device manager if there are equipment pops up

N

Y

Re download。

Y

Replace memory

Y

Replace CPU

CTP problem

The CTP test is normal?

Replace the CTP

The replacement of a CTP have a look is a touch screen or motherboard problem?

Replace CTP

CTP connectors, welding of EMI filter is a problem?

Y

N

N

Y

Welding connector or EMI filters

Replace the CPU

Using the oscilloscope observation, I2C control line CTP IF signal is given.

N

N

Replace the PMIC

OK

Replace charger

The charger is plugged in, no charge indicator

N

Y

Replace the battery is normal? Measure the batteryvoltage is less than 3V

Replace the battery

Y

N

Check the OVP IC USB connector and peripheral devices, whether the welding is good? After re welding is normal

Y

OK

N

Replace the charger or the data line is the normal charge?

Y

Replace charger

Insert the USB line, the port was not found in thecomputer

N

Y

Replace the battery is normal? Measure the batteryvoltage is less than 3V

Replace battery

Y

N

Check OVP, USB connector and peripheral device is the welding is good? After re welding is normal

Y

OK

N

Replace the charger or the data line is the normal charge?

Replace PMIC

Y

OK

White or black screen no display, backlight light

Check the motherboard EMI device LCD pathway of welding and weldingpower supply is normal, EMI filter。

OK

Check the LCD other peripheral devices are weld, check whether LCDconnector.

Check the LCD FPC connection is good, re assembly of FPC mobile phone is normal

N

N

Y

OK

Y

Replacing LCD, display is normal，

N

OK

Y

Y

Welding weld device

N

Replace CPU

Inspection should be light in the case of LCD amount of backlight driveoutput voltage pin pin to whether a voltage exceeding 20V

OK

Backlight circuit is normal, LCD problem

Check the backlight driver and peripheral device welding

Y

N

Y

Y

OK

Check the LCD module FPC with connector on the motherboardconnection well, reconnect whether normal

N

LCD No backlight

Replacing the LCD again to verify LCD backlight is on.

OK

Y

N

Power supply memery and CPU to check whether the normal.

Y

N

Y

Y

Welding related circuit device and PMIC

Connected to the computer through the USB line, check the computer device manager if there are equipment pops up

N

dead

Y

N

Re-download

Check the 32KHz crystal is normal? Whether the 32KHzsignal?

Welding and try again

Welding and try

Check the 19.2MHz crystal is normal? Whether the 32KHz signal?

N

The relevant circuit, check the memery to replace the memery, to see whether the normal?

Ok

Y

N

Replace CPU

No key

N

Replace CPU

Assembly check button FPC or welding, welding or reinstall again

Press the button, the detection signal line to ground short circuit.

N

Replace key

Y

OK

Y

Replace CPU

Bad display screen

Check the motherboard EMI device LCD pathway of welding and welding power supply is normal, EMI filter.

OK

Check the LCD other peripheral devices are weld, check whether LCDconnector.

Check the LCD FPC connection is good, re assembly of FPC mobile phone is normal,

N

N

Y

OK

Y

Replacing LCD, display is normal，

N

LCD problem

Y

Y

Welding weld device

N

NO SPK

N

Y

OK

N

Check the receiver circuit bead welding is normal. Re welding test

Test the speaker impedance is 8 ohms or 4 ohm

Check whether the speaker spring contact point and good contact. Reassembly test to see whether the normal。

Y

OK

The speaker has a problem, replacing the speaker

N

To change the audio codec chip

small bell

N

Y

OK

N

Check the speaker circuit bead welding is normal. Re welding test

Test the speaker impedance is 8 ohms or 4 ohm

Check whether the speaker spring contact point and good contact. Reassembly test to see whether the normal.

Y

OK

The speaker has a problem, replacing the speaker

N

To change the audio codec chip

Re burning software, see audio parameter is missing or replacement

Y

N

Y

OK

Replace the battery charger

The charger is plugged in, can not charge

N

Y

Replace the battery is normal? Measure the batteryvoltage is less than 3V

Replace battery

Y

N

Check the OVP IC USB connector and peripheral devices, whether the welding is good? After re welding is normal

Y

OK

N

Replace the charger or the data line is the normal charge?

Replace PMIC

OK

Can't take pictures

OK

Check the EMI device is complete, good welding？

N

Y

N

Y

Welding and try again

N

Replace the Camera module is OK

Check the Camera module connector is good welding, welding connector is OK?

N

Y

OK

Teardown check whether Camera module from the module, reinstall OK

N

Y

OK

Check the main chip welding normal?

Welding or replacement

Automatic shutdown

N

Y

According to Download Tool, poor positioning components

N

To Download program, to see whether the Download completed

Check the battery has power, battery temperature detection pin,connector is good

With the power on, to see whether the electric current is normal

Y

Check whether the device has been damaged

To charge the battery, replace the connector

Y

Check whether the software version, SN, IMEI information can be read out

N

N

The modem chip is good

Y

N

The charge is normal

Check the charging chip is good

Y

N

Check if CPU is good

The board leakage

The module of leakage, OK

N

Replace the relevant module IC and a power supply filter capacitor,leakage has disappeared

Gradually remove various peripherals, each having a connector is connected or connected by FPC LCD, camera, look at the electric leakageon the motherboard

Y

The temperature rise device power supply screening larger, determining the short circuit power supply network

Y

Replace PMIC

Plus electric will not boot, observe whether there is a large leakagecurrent appears

Can determine the electric leakage in the direct power supply batteryVBAT

Boot machine apart after power on, all parts of the PCB board by handtouch, whether the device temperature seriously, to determine a preliminary rough location leakage device

N

Y

Power supply using a multimeter to screening of various modules of theresistance to ground, screening out the power supply network resistancesmall

Y

N

N

Backlight module of direct power Vbat driver, PA screening, or directly off,determine the leakage module

The peripheral module leakage, replacement